## Slide 1
TELECOM TRACE ANALYSIS / PRODUCT BRIEF
TraceScope
From raw network records to an engineer-readable subscriber journey.
A local-first workbench for LMT user traces, protocol context, and technology-aware network paths.
UE
subscriber
→
RAN
radio access
→
CORE
control
→
DATA
service

## Slide 2
TRACESCOPE / CORE NETWORK TRACE WORKBENCH
The trace is evidence. The engineer needs the story.
ENGINEER PRODUCT OVERVIEW · 05 OCT 2026
02
RAW EXPORT
Binary containers, internal labels, protocol messages, and node positions arrive together.
ENGINEERING FRICTION
Finding the right event and following signaling across technologies takes repeated manual inspection.
TRACE SCOPE
A guided timeline, message inspector, call flow, and infrastructure route keep evidence in one review surface.
Make each record easier to locate, read, and relate to its neighbors.
TraceScope is an analysis aid—not a full vendor dissector or live network inventory. It separates values found in the file from protocol-based interpretation.

## Slide 3
TRACESCOPE / CORE NETWORK TRACE WORKBENCH
One workflow, from import to reviewable evidence
ENGINEER PRODUCT OVERVIEW · 05 OCT 2026
03
01 · IMPORT
Open PTMF or supported text trace. Parsing runs in the browser.
→
02 · MAP
Inspect time, position, message type, direction, and payload boundary.
→
03 · FOLLOW
Move through timeline, sequence flow, and technology-aware route.
→
04 · EXPLAIN
Read telecom context, consult references, and capture findings.
Unknown fields remain unknown; no successful procedure is inferred from a request alone.

## Slide 4
TRACESCOPE / CORE NETWORK TRACE WORKBENCH
A message inspector built for telecom context
ENGINEER PRODUCT OVERVIEW · 05 OCT 2026
04
MESSAGE TIMELINE
16:13:04.395
SGsAP-PAGING-REQUEST
MSC → MME
16:13:04.402
S1AP · PAGING
MME → eNodeB
16:13:04.671
EXTENDED SERVICE REQUEST
UE → MME
16:13:04.672
MM_SGSAP_SERVICE_REQ
Internal · vendor label
OBSERVED FIELDS
Timestamp · node/LMT · direction if decoded · property · type/code · size · offset · bytes
TELECOM KNOWLEDGE
Plain-language message role, basis, and 3GPP reference appear beside the selected record. Explanations state what the message alone cannot prove.

## Slide 5
TRACESCOPE / CORE NETWORK TRACE WORKBENCH
Follow the route across the detected technology
ENGINEER PRODUCT OVERVIEW · 05 OCT 2026
05
2G
MS
reference component
→
BTS
reference component
→
BSC / PCU
reference component
→
MSC / SGSN
reference component
→
GGSN
reference component
3G
UE
reference component
→
Node B
reference component
→
RNC
reference component
→
SGSN
reference component
→
GGSN
reference component
4G
UE
reference component
→
eNodeB
reference component
→
MME / SGW
reference component
→
PGW
reference component
→
PDN
reference component
5G
UE
reference component
→
gNodeB
reference component
→
AMF / SMF
reference component
→
UPF
reference component
→
DN
reference component
Green = observed match
Gold dashed links in the app = inferred standard topology

## Slide 6
TRACESCOPE / CORE NETWORK TRACE WORKBENCH
Keep the evidence boundary visible
ENGINEER PRODUCT OVERVIEW · 05 OCT 2026
06
OBSERVED
Values read from record containers or explicit endpoints: timestamp, position, type/code, length, and available direction.
MAPPED
Known signatures associate a record with a likely technology or route segment. The UI labels these associations as observed or inferred.
EXPLAINED
Message knowledge describes the protocol role and states when a response, cause code, or decoded information element is needed.
A request is not proof of success. A vendor-internal label is not a decoded information element.

## Slide 7
TRACESCOPE / CORE NETWORK TRACE WORKBENCH
Engineer tools with explicit data boundaries
ENGINEER PRODUCT OVERVIEW · 05 OCT 2026
07
AI ASSISTANT
Text and browser-supported voice
Trace-grounded questions with record citations
Local viewer commands stay local
NVIDIA GLM-5.3 via local server
RESEARCH DESK
Explicit Huawei-focused Tavily search
Huawei-domain filter
Saved sources and documents in browser storage
AUDIT & EXPORT
Activities separated from why/decisions
Browser-local audit trail
Trace and audit JSON export
Selected trace context is sent to NVIDIA when asking AI questions. Web research is user-triggered.

## Slide 8
TRACESCOPE / CORE NETWORK TRACE WORKBENCH
A practical engineer walkthrough
ENGINEER PRODUCT OVERVIEW · 05 OCT 2026
08
1
Import the trace
Confirm record count, timestamp range, and detected technologies.
2
Locate a message
Search by record number, protocol, type, or node.
3
Inspect the evidence
Read fields, telecom information, basis, and raw bytes.
4
Follow the procedure
Open Call flow or Network path; step or animate.
5
Capture findings
Ask a question, check the audit trail, export JSON.
Validate conclusions with a qualified dissector, applicable 3GPP release, and network-side evidence.